## Slide 1: Decarbonizing Water Desalination with Renewable Energy and Battery Storage Using Optimization Algorithms
Om Sanan
December 2024

## Slide 2: Vision
Vision
  Resilient Water Supply Infrastructure
    Water Security and Energy Independence
  Decarbonization Desalination
    Hybrid Renewable Energy and Battery Storage
  AI-driven Solutions
Uniqueness
  Decarbonization solution for new and existing water desal. plants
    4 Real-life desal plants case studies
  Creation of an Automated Energy Management System (EMS) that can:
    Process data from multiple sources in real time
    Automatically obtain data via APIs
    Use ML forecasting models & optimization algorithms to align RE generation with energy demand on an hourly basis

## Slide 3: Background
Global Water Scarcity 2 billion (26%) people lack access to clean water— expected to double by 2050 (U.N.) Global Warming and Population growth are exacerbating the issue | Problem Statement Desalination can provide an abundant source of water, however, it is: Expensive: Energy is 40% of total desal. cost Results in significant carbon emission
Renewable Energy & Battery Storage Abundant RE source; can replace 100% electricity RE cost has reduced ~80% over the last decade Currently powers only 1% of Desalination High initial CAPEX & Intermittent nature of RE Battery storage: Facilitates the efficient utilization of RE, enabling grid stabilization, peak shaving, and load shifting but expensive | Gap in Research / Problem Statement Current studies use data that is either simulated or collected on a small scale Lack comprehensive assessment of multiple RE sources and optimization

## Slide 4: Research Overview
Objective: Obtain the optimal system sizing of hybrid RE sources and battery storage to decarbonize desalination
  Minimizing cost and carbon footprint
  Protects against energy price volatility
  Obtain energy independence
Real-life, mid-large size desalination plants
Systems Evaluated: PV, CSP, Wind Energy, Hydro Energy, Battery Storage
Methods: (i) Sophisticated ML models to forecast water demand, energy consumption, and weather/environmental data; and (ii) Optimization algorithms to design an optimal RE and battery mix

## Slide 5: Summary of Four Desalination Facilities
Desalination facilities:
Alameda, CA
Hutchinson, TX
SAWS, TX
Tampa Bay, FL
Combined electricity usage = 75 million kWh
Conversion to 100% RE = ↓ 32,000 metric tons of annual carbon emissions = planting 1.2 million trees
https://www.nrel.gov/gis/assets/images/solar-annual-ghi-2018-usa-scale-01.jpg
Tampa Bay
SAWS
Hutchinson
Alameda

## Slide 6: Desalination Plant Data

## Slide 7
Methodology
Forecasting Inputs (2023-2027)
Energy Consumption & Treated Water
Wind, Temperature, and Solar Irradiance
Estimate RE Generation for Wind, PV, and CSP
Multi-objective Optimization
Minimize CO2
Minimize Cost
Step 1
Step 2
Step 3
Total Cost & CO2 Emissions for RE & BS
Step 4

## Slide 8
Methodology
Forecasting Inputs (2023-2027)
Energy Consumption & Treated Water
Wind, Temperature, and Solar Irradiance
Estimate RE Generation for Wind, PV, and CSP
Multi-objective Optimization
Minimize CO2
Minimize Cost
Step 1
Step 2
Step 3
Total Cost & CO2 Emissions for RE & BS
Step 4

## Slide 9: Forecast Treated Water, Energy Usage, Weather
Forecast of Daily Treated Water Flows and Energy Consumption
  Data Used: Rainfall, Hours in Operation, Raw Water Flows, Backwash Water Usage, Peak Demand, Avg Turbidity, Max Turbidity
  Data Forecast: Water Flows, Energy Consumption
  Models Used: SARIMA, Random Forest, XGBoost, Gradient Boosting, Ensemble
Forecast of Weather Data (Climate & Hydro)
  Why: To determine RE generation potential
  Data Used: Temperature, Solar Irradiance, Humidity, Wind Speed
  Data Forecast: Solar Irradiance, Wind Speed, Temperature
  Models Used: XGBoost, LSTM, Linear/Polynomeal Regression

## Slide 10: Forecast Treated Water/Energy Consumption
Daily/monthly 5-year data from desal plants: energy use, water flow, TDS, turbidity, temperature, pH
Preprocessing/Feature Engineering: Log transformations, lag creation, train/test split
Model Training
  Regression based models: Random Forest, Gradient Boosting, SARIMA
  Hyperparameter tuning through GridSearchCV (cross-validation)
Model Forecast
  Used each model to obtain test set predictions
  Ensemble approach - averages model predictions to mitigate individual model biases

## Slide 11
Treated Water & Energy Consumption (Tampa Bay)
Daily Energy Consumption (kWh)
Total Treated Water (MGD)
Training Data: 2017-2021
Test Data: 2022-2023

## Slide 12
Forecast Treated Water & Energy (Tampa Bay)
Model Forecast: 2023-2027

## Slide 13: Forecast Wind Speed/Temperature/GHI
Integrated into Streamlit application
Data Preparation and Preprocessing
  20 year hourly climate data using NSRDB API
  60:20:20% split for Training:Testing:Validation
Feature Engineering: Lag Features, Rolling Window Statistics, Differencing
Model Training and Validation
  Parameter Tuning: Use grid search to find optimal parameters
  XGBoost: Employs gradient boosting decision trees
  Prophet: Daily observations with strong seasonal effects; time-series forecating
  Average Method: Forecasts future values as the average of past observations
  Autoregressive Validation: Past data points as inputs to forecast
Forecasting: Iterative Forecast + Optional Noise Injection

## Slide 14
Forecast Wind Speed, Temp., GHI (Tampa Bay)
XGBoost Average Method Model
Test data used to validate the accuracy of the training model
GHI (W/m2)
Training Data: 1998-2016
Test Data: 2017-2021
Avg Validation Plot for GHI_Diff

## Slide 15: Wind Speed/Temperature/GHI Forecast Trends
Monthly temperature and wind speed expected trends (2023-2027)
Average monthly solar irradiance expected trends (2023-2027)

## Slide 16: Daily and Seasonal Trends in Weather

## Slide 17: Results: Forecasted Variable Error Rates (RMSE)
Forecasted models show normalized Root Mean Square Error of less than 10% for key metrics such as treated water flows, energy demand, temperature, and wind speed, and less than 20% for solar irradiance (GHI)

## Slide 18
Methodology
Forecasting Inputs (2023-2027)
Energy Consumption & Treated Water
Wind, Temperature, and Solar Irradiance
Estimate RE Generation for Wind, PV, and CSP
Multi-objective Optimization
Minimize CO2
Minimize Cost
Step 1
Step 2
Step 3
Total Cost & CO2 Emissions for RE & BS
Step 4

## Slide 19
Step 2: RE and BS Generation Formulas

## Slide 20: Step 2: RE and BS - Variables and Constants

## Slide 21: Results: RE Generation Forecast
Forecast Temperature, Wind Speed, GHI (solar irradiance)
Calculated Renewable Energy Generation

## Slide 22
Methodology
Forecasting Inputs (2023-2027)
Energy Consumption & Treated Water
Wind, Temperature, and Solar Irradiance
Estimate RE Generation for Wind, PV, and CSP
Multi-objective Optimization
Minimize CO2
Minimize Cost
Step 1
Step 2
Step 3
Total Cost & CO2 Emissions for RE & BS
Step 4

## Slide 23: RE CAPEX, OpEx, CO2 Emissions: Assumptions
is Fixed Annual Payment per Unit (CAPEX amortized/25 years + annual Fixed OH)
T
Source:
CAPEX, FOH, VOH, are sourced from NREL Annual Technology Baseline Database 2023
Lifetime CO2 emissions are sourced from NREL
High-end RE system specs are sources from leading vendors of RE systems

## Slide 24
Methodology
Forecasting Inputs (2023-2027)
Energy Consumption & Treated Water
Wind, Temperature, and Solar Irradiance
Estimate RE Generation for Wind, PV, and CSP
Multi-objective Optimization
Minimize CO2
Minimize Cost
Step 1
Step 2
Step 3
Total Cost & CO2 Emissions for RE & BS
Step 4

## Slide 25: Optimizing the RE Supply and Plant Energy Demand
Desalination Plant - Treated Water + Energy Consumption Forecasting
Weather / Solar Radiation
Forecasting
Renewable Energy
Parameters
Multi-objective Optimization
Engine
Optimal RE & Battery Storage Mix for each Desalination Plant
Minimize Cost
Minimize CO2

## Slide 26: Optimization Algorithm Overview
Wind
PV
CSP
nwt
npv
ncsp
Number of units
Battery
nb
Battery
Charging
Battery
Usage
Desalination Plant Energy Demand
Optimization algorithm calculates optimal energy mix to supply the energy demand, as well as battery capacity on a monthly basis in 2023-2027.
Utility
Utility is used when battery + RE cannot meet the demand
Unit Capacity
(Forecasted hourly for each location)

## Slide 27: Optimization Scenarios
Scenario 1: 100% RE with Battery Storage (No Utility)
  Grid independence
Scenario 2: 50-100% RE-mix with Utility (No Battery Storage)
  Transition towards grid independence
Scenario 3: 0-30% RE with Utility (No Battery Storage)
  Test benefits of partial RE adoption
  All Scenarios assume no net metering

## Slide 28: PSO Optimization Model
Population-based stochastic optimization technique inspired by the social behavior of birds flocking or fish schooling
Objective Function: minimize cost and CO2 emissions, where and are both 50%
Cost of $50/ton has been assumed for CO2 Emissions
Particle Swarm Optimization:
The position of each particle xi is updated according to:

## Slide 29: NSGA-II Optimization Model
NSGA-II Non-dominated Sorting Genetic Algorithm
Suitable for multi-objective optimization.
Similar to a typical genetic algorithm, with a modified mating and survival selection
Optimization algorithm calculates the number of units for wind turbines, photovoltaic panels, CSP systems, and batteries for each month
nwt
npv
ncsp
nb
Optimize for Cost
Optimize for CO2 Emissions
Forward Model Summary
Inverse Model Summary

## Slide 30: NSGA-II Optimization Model
Optimum nwt, npv, ncsp, and nb for each month
Optimum nwt, npv, ncsp, and nb for each year (2023-2027)
Optimum nwt, npv, ncsp, and nb for the entire 5-year duration (2023-2027)
Main Loop on Month and Year

## Slide 31: PSO Model - Optimization Results (Tampa Bay)
Optimization of Scenarios 1, 2 and 3 result in: 100%, 99%, and 30% RE mix, respectively, and produce excess energy of 11%, 15%, and 0%, respectively (as there is no net metering)

## Slide 32: PSO Model - Optimization Results (Tampa Bay)
5-year Total Cost of Scenario 2, 3, Baseline (100% Utility) is ~$16.9 million, whereas Scenario 1 is ~$25 million due to use of 12 batteries to create 100% energy independence.
CO2 Emissions (grams/kWh) of Scenario 1, 2, 3, Baseline = 5M, 1.4B, 62.5B, 90B, resp.

## Slide 33: Potential Limitations
There is uncertainty in forecasted water/energy/weather data
We did not account for plant downtime in model training for energy consumption and water flows
This study takes into account PV, Wind, CSP, and Battery Storage.
  Future Studies can include Geothermal Energy and Hydrogen Storage

## Slide 34: Conclusions
Key Achievements
  Established a robust framework and formulas for optimizing RE integration in desalination
  Water production, energy consumption, and weather forecasting using AI models to calculate RE generation
  Multi-objective optimization algorithim for optimal mix of RE investments needed to supply a desalination plant for a given region.
Future Study
  Perform sensitivity analysis for optimization mix of RE system and battery storage

## Slide 35: Acknowledgement
Dr. Joshua Sperling National Renewable Energy Laboratory Manager – New Concepts Incubator, Urban Futures and the Energy-X Nexus Colorado | David Greene National Renewable Energy Laboratory Water, Energy, Climate, and Sustainability Engineer and Program Manager Colorado | Ross Greer UC – San Diego PhD Candidate - Electrical & Computer Engineering California